## Slide 1
Active Reconfigurable Intelligent Surface:
Fully-Connected or Sub-Connected?
Based on the paper by Kunzan Liu, Zijian Zhang, Linglong Dai, et al. (Tsinghua University)
Paper Review Presentation
Presenter: Hengrui Pei
Date: 12/12/2025

## Slide 2
Introduction & Motivation
From Passive Fading to Active Power Consumption

## Slide 3
Passive RIS
Reconfigurable Intelligent Surface,is a new technology that can control how wireless signals propagate in the environment. Passive RIS only reflects signals and suffers from multiplicative fading.
Active RIS (Fully-Connected)
Active RIS introduces amplifiers to enhance signal strength.
The New Problem
The fully-connected architecture consumes excessively high power, with static power consumption rivaling the base station itself.
The Evolution of RIS Technology

## Slide 4
The Sub-Connected Architecture
In this project, I adopt and investigate a sub-connected architecture, where multiple RIS elements (T) share one power amplifier, targeting energy-efficient system design.
Key Hypothesis of This Project: The performance loss due to fewer DoFs is minor, while the energy efficiency gain is significant.
Pro: Drastically reduces the number of amplifiers (from N to L=N/T), saving significant power.
Con: Beamforming has fewer controllable degrees of freedom (DoFs). (Loss in beamforming flexibility)
■
■
Proposed Solution: Sub-Connected Architecture
This architecture is selected in this project specifically for energy-efficiency-oriented design.

## Slide 5
Fully-Connected (Baseline)
Each element has a dedicated power amplifier (PA) and phase shifter (PS).
1 Element → 1 PA → 1 PS
Amplifiers (L): L = N Power: High (N * W_PA) DoFs: High
Sub-Connected (Proposed)
A group of 'T' elements shares one PA. Each element retains its own PS(Phase Shifter).
1 PA → T Elements / T PS
Amplifiers (L): L = N / T Power: Low ((N/T) * W_PA) DoFs: Reduced
Architecture & Power Model Comparison

## Slide 6
Innovation & Contributions
I focus on optimizing energy efficiency rather than only spectral efficiency.
A sub-connected active RIS is designed to reduce the number of power amplifiers from N to N/T
A joint EE optimization framework (Dinkelbach + alternating optimization) is developed.
An independent SE–EE trade-off is verified (≈11% SE loss vs. ≈21% EE gain).

## Slide 7
Methodology
Maximizing Energy Efficiency (EE) via Joint Beamforming

## Slide 8
The Problem
The goal is to maximize Energy Efficiency: η = Rate / Power. This is a complex non-convex fractional programming problem.
Dinkelbach's Algorithm
The fractional problem max(R/P)` is transformed into a subtractive form `max(R - η*P)` which can be solved iteratively.
Alternating Optimization
The problem is solved by optimizing each set of variables (W, Θ, a) one at a time, keeping the others fixed, until convergence.
Optimization Strategy
Notes: Dinkelbach Algori transform a multiplication problem into a subtraction problem
beamforming matrix W, the RIS phase shifts Θ, and the amplification coefficients

## Slide 9
Fractional Programming with Dinkelbach
Objective (difficult fractional form):
Dinkelbach transformation:
Energy Efficiency (EE) = rate / power → fractional and non-convex
Dinkelbach method converts fraction into subtracting form
In each outer iteration, η is updated
This turns a hard fractional program into a sequence of easier subproblems
Guarantees convergence to optimal EE under mild conditions

## Slide 10
Alternating Optimization
Begin by initializing all variables, including the BS beamforming matrix W, the RIS precoding Ψ赛, and the auxiliary variables μ and ν.
Step 1: Update the auxiliary variables μ and ν using their closed-form expressions.
These variables help reformulate the log-rate expression and make the objective easier to optimize.
Step 2: With μ and ν fixed, update the BS beamforming matrix W by solving a QCQP sub-problem.
Step 3: With W fixed, update the RIS precoding Ψ, which includes computing both the phase-shift vector Θ and the amplification vector a using closed-form solutions.
After the three updates, checking the convergence criteria based on the change in energy efficiency.
If the objective has not converged, the algorithm repeats the steps above; otherwise, it outputs the optimal energy efficiency.

## Slide 11
Simulation Results
Validating the Sub-Connected Architecture

## Slide 12
Simulation Results

## Slide 13
Spectral Efficiency (SE)
~11% Loss
The sub-connected architecture has about an 11% lower data rate than the fully-connected one due to fewer DoFs.
Energy Efficiency (EE)
~22% Gain
In this project, this slight SE loss is traded for a significant 22% increase in energy efficiency, validating the proposed design.
The Key Trade-Off (T=16 vs. T=1)

## Slide 14
Energy Efficiency increases as more elements (T) share a single amplifier. In this setup, T=256 (one amp for all elements) was the most efficient.
Impact of Group Size (T) on Energy Efficiency

## Slide 15
Proposed: In this project, I study a novel sub-connected architecture for active RIS to address the high power consumption problem.
Mechanism: Power is saved by sharing one amplifier among 'T' elements, at the cost of reduced beamforming DoFs.
Results: Through independent simulation, about 22% higher EE is achieved with only about 11% SE loss.
Conclusion: This project demonstrates that the sub-connected architecture is a practical and energy-efficient realization of active RIS.
Conclusion

## Slide 16
Thank you !